        Polypropylene

Chemical Formula :- (C3H6)n
Polypropylene (PP), also known as polypropene, is a thermoplastics polymer used in a wide variety of applications. It is produced via chain growth polymerisation from the monomer polypropylene
Polypropylene belongs to the group of polyolefins and is partially crystalline and non-polar. Its properties are similar to polyethelene, but it is slightly harder and more heat resistant. It is a white, mechanically rugged material and has a high chemical resistance.Polypropylene is the second-most widely produced commidity plastic (after polyethylene) and it is often used in packaging and labeling. In 2013, the global market for polypropylene was about 55 million .
History:-
Phillips petrolium chemists J.paul Hogan and Robert banks first polymerized propylene in 1951. Propylene was first polymerized to a crystalline isotactic polymer by Giulio natta as well as by the German chemist Karl Rehn in March 1954. This pioneering discovery led to large-scale commercial production of isotactic polypropylene by the Italian firm Montecatini from 1957 onwards. Syndiotactic polypropylene was also first synthesized by Natta and his coworkers.
After polyethylene, polypropylene is the most important plastic with revenues expected to exceed US$145 billion by 2019. The sales of this material are forecast to grow at a rate of 5.8% per year until 2021
Chemical and Physical Properties:-

Polypropylene is in many aspects similar to polyethylene, especially in solution behaviour and electrical properties. The methyl group improves mechanical properties and thermal resistance, although the chemical resistance decreases.:19 The properties of polypropylene depend on the molecular weight and molecular weight distribution, crystallinity, type and proportion of comonomer (if used) and the isotactivity In isotactic polypropylene, for example, the methyl groups are oriented on one side of the carbon backbone. This arrangement creates a greater degree of crystallinity and results in a stiffer material that is more resistant to creep than both atactic polypropylene and polyethylene

Mechanical Properties:-
The density of (PP) is between 0.895 and 0.92 g/cm³. Therefore, PP is the commidity plastic with the lowest density. With lower density, moldings part with lower weight and more parts of a certain mass of plastic can be produced. Unlike polyethylene, crystalline and amorphous regions differ only slightly in their density. However, the density of polyethylene can significantly change with fillers.:24
The Young modulus of PP is between 1300 and 1800 N/mm².
Polypropylene is normally tough and flexible, especially when copolymerised with ethylene. This allows polypropylene to be used as an engineering plastic, competing with materials such as acrylonitrile butadiene styrene (ABS). Polypropylene is reasonably economical.[citation needed]
Polypropylene has good resistance to fatigue
### Thermal properties
The melting point of polypropylene occurs in a range, so the melting point is determined by finding the highest temperature of a differential scanning calorimetry chart. Perfectly isotactic PP has a melting point of 171 °C (340 °F). Commercial isotactic PP has a melting point that ranges from 160 to 166 °C (320 to 331 °F), depending on atactic material and crystallinity. Syndiotactic PP with a crystallinity of 30% has a melting point of 130 °C (266 °F).[8] Below 0 °C, PP becomes brittle.[9]
The thermal expansion of polypropylene is very large, but somewhat less than that of polyethylene
### Chemical properties
Polypropylene at room temperature is resistant to fats and almost all organic solvents, apart from strong oxidants. Non-oxidizing acids and bases can be stored in containers made of PP. At elevated temperature, PP can be dissolved in nonpolar solvents such as xylene, tetralin and decalin. Due to the tertiary carbon atom PP is chemically less resistant than PE (see Markovnikov rule).[10]
Most commercial polypropylene is isotactic and has an intermediate level of crystallinity between that of low-density polyethylene (LDPE) and high-density polyethylene (HDPE). Isotactic & atactic polypropylene is soluble in P-xylene at 140 °C. Isotactic precipitates when the solution is cooled to 25 °C and atactic portion remains soluble in P-xylene.
The melt flow rate (MFR) or melt flow index (MFI) is a measure of molecular weight of polypropylene. The measure helps to determine how easily the molten raw material will flow during processing. Polypropylene with higher MFR will fill the plastic mold more easily during the injection or blow-molding production process. As the melt flow increases, however, some physical properties, like impact strength, will decrease.
There are three general types of polypropylene: homopolymer, random copolymer, and block copolymer. The comonomer is typically used with ethylene. Ethylene-propylene rubber or EPDM added to polypropylene homopolymer increases its low temperature impact strength. Randomly polymerized ethylene monomer added to polypropylene homopolymer decreases the polymer crystallinity, lowers the melting point and makes the polymer more transparent.

Manufacturing technique of Polypropylene :-
Polypropylene is currently one of the fastest growing polymers. Much of this growth is attributed to polypropylene’s ability to displace conventional materials (wood, glass, metal) and other thermoplastics at lower
cost. Polypropylene (PP) is a tough, rigid plastic and produced in a variety of molecular weights and crystallinities.
Polypropylene is made from the polymerization of propylene gas in the presence of a catalyst system, usually Ziegler-Natta or metallocene catalyst. Polymerization conditions (temperature, pressure and reactant concentrations) are set by the polymer grade to be produced.
Various production processes exist with some general similarities. They are taking place either in a gas-phase (fluidized bed or stirred reactor) or a liquid-phase process (slurry or solution). An example of flow diagram corresponding to each of the two types of processes is illustrated in figure 1 bellow. The gas-phase polymerization is economical and flexible and can accommodate a large variety of catalysts. It is the most common technology in modern polypropylene production plants. Relevant technologies are Novolen®, Unipol® (gas-phase processes), Borstar® and Spheripol® (liquid-phase processes)
Utilization :-
      It is used in a variety of applications to include packaging for consumer products, plastic parts for various industries including the automotive industry, special devices like living hinges, and textiles.

Environmental Impact :-
        Manufacturing PP fiber from polypropylene is a process with low impact on the environment—no toxic waste, no toxic emissions, no fluorocarbons and no halogens. The manufacture of products from PP staple fiber has low environmental impact: ... No toxic emissions or wastes.

Health Impact :-
      Type 5: Polypropylene - Safe. Polypropylene containers do not leach harmful chemicals into foods or liquids. They commonly contain yogurt, medicine, drinks, ketchup and medicines. Type 5 plastic is flexible, hard and semi-transparent and has high resistance to solvents.

Alternative :-
  organic materials like jute or hemp are used as alternatives to solid-weave polypropylene in earthbag construction. However, the sustainable idea somehow conflicts with the purpose of earthbags. Polypropylene is chosen for its low cost and its resistance to water damage, rot, and insects.

Biodegradibility :-
        A PP part would last many many years in the soil. It is not toxic by itself but if an animal eat a PP part it could stay in its stomach, endangering his life.
        A reasonable proportion of polypropylene is recycled from major industries, but a significant proportion is still dumped into landfills. It is currently not as economically viable to recycle PP as it is to recycle other polymers, in particular HDPE, LDPE and PET.

        Polypropylene image